## Slide 1
MODULE 4
PROJECTION

## Slide 2
Introducing the idea of projecting 3D object on to 2D plane;
broad classification – parallel & perspective projection; different types of parallel projection & examples of each;
formal definition of 3D to 2D projection and derivation of projection matrix;
1-point, 2-point &3-point perspective projection;
formal derivation of vanishing point(s) and physical implication of the same.
CONTENTS

## Slide 3
Introducing the idea of projecting 3D object on to 2D plane
It is the process of converting a 3D object into a 2D object.
Leonhard Euler Around in 1756
Episcope – first projection system.
It is also defined as mapping or transformation of the object in projection plane or view plane.
The view plane is displayed surface.

## Slide 5
PARALLEL PROJECTION
Parallel Projection use to display picture in its true shape and size.
When projectors are perpendicular to view plane then is called orthographic projection.
The parallel projection is formed by extending parallel lines from each vertex on the object until they intersect the plane of the screen.
The point of intersection is the projection of vertex.
Parallel projections are used by architects and engineers for creating working drawing of the object, for complete representations require two or more views of an object using different planes.

## Slide 6
In the 2D system, we use only two coordinates X and Y but in 3D, an extra coordinate Z is added.
3D graphics techniques and their application are fundamental to the entertainment, games, and computer-aided design industries.
It is a continuing area of research in scientific visualization.
Furthermore, 3D graphics components are now a part of almost every personal computer and, although traditionally intended for graphics-intensive software such as games, they are increasingly being used by other applications.

## Slide 8
Characteristic of parallel Projection:
In parallel Projection, the projection lines are parallel to each other.
There is the least amount of distortion within the object.
The lines that are parallel to the object are also parallel to the drawing.
The view of Parallel Projection is the less realistic cause of no foreshortening.
The Parallel Projections are good for accurate measurements.

## Slide 9
ORTHOGRAPHIC PROJECTION
The orthographic projection is derived from the principles of descriptive geometry and is a two-dimensional representation of a three-dimensional object.
It is a parallel projection (the lines of projection are parallel both in reality and in the projection plane).
It is the projection type of choice for working drawings.
If the normal of the viewing plane (the camera direction) is parallel to one of the primary axes (which is the x, y, or z axis),
the mathematical transformation is as follows; To project the 3D , onto the 2D point using an orthographic projection parallel to the y axis (where positive y represents forward direction - profile view), the following equations can be used:
where the vector s is an arbitrary scale factor, and c is an arbitrary offset. These constants are optional, and can be used to properly align the viewport.

## Slide 10
ORTHOGRAPHIC PROJECTION
Using matrix multiplication, the equations become:
While orthographically projected images represent the three dimensional nature of the object projected, they do not represent the object as it would be recorded photographically or perceived by a viewer observing it directly.
In particular, parallel lengths at all points in an orthographically projected image are of the same scale regardless of whether they are far away or near to the virtual viewer.
As a result, lengths are not foreshortened as they would be in a perspective projection.

## Slide 11
ORTHOGRAPHIC PROJECTION
Multiview Orthographic Projection:
In Multiview Orthographic Projection, we can represent the two-dimensional Orthographic image into a three-dimensional object.
The Multiview Orthographic Projection Includes-
Front View
Top View
Side View

## Slide 12
AXONOMETRIC PROJECTION
A types of orthographic projection.
Used for creating a pictorial drawing of an object, where lines of sight are perpendicular to the plane of projection.
The object is rotated around one or more of its axes to reveal multiple sides.

## Slide 13
AXONOMETRIC PROJECTION
"Axonometry" means "to measure along axes"
The three types of axonometric projection are isometric projection, dimetric projection, and trimetric projection, depending on the exact angle at which the view deviates from the orthogonal.
Typically in axonometric drawing, as in other types of pictorials, one axis of space is shown as the vertical.

## Slide 14
In isometric projection, The term "isometric" comes from the Greek for "equal measure", reflecting that the scale along each axis of the projection is the same
AXONOMETRIC PROJECTION
An isometric view of an object can be obtained by choosing the viewing direction such that the angles between the projections of the x, y, and z axes are all the same, or 120°.
Line of sight are parallel to each other and perpendicular to the plane of projection.
Distance between object and observer is infinite.
Object is rotated along its axis relative to the plane of projection to show all three dimensions in only one view..

## Slide 15
AXONOMETRIC PROJECTION
In dimetric projection, the direction of viewing is such that two of the three axes of space appear equally foreshortened, of which the attendant scale and angles of presentation are determined according to the angle of viewing; the scale of the third direction is determined separately. Dimensional approximations are common in dimetric drawings.

## Slide 16
AXONOMETRIC PROJECTION
In trimetric projection, the direction of viewing is such that all of the three axes of space appear unequally foreshortened. The scale along each of the three axes and the angles among them are determined separately as dictated by the angle of viewing. Dimensional approximations in trimetric drawings are common and trimetric perspective is seldom used in technical drawings.

## Slide 18
OBLIQUE PROJECTION
Oblique projection is a simple type of technical drawing of graphical projection used for producing two-dimensional images of three-dimensional objects.
Oblique projection can also be described as a parallel projection in which the projection lines are not orthogonal to the projection line.
Oblique projection is a form of parallel projection.
Usually, the presence of one or more 90 angles within a pictorial image is usually a good indication that the perspective is oblique.
In oblique projection, the projector lines form oblique angles (non-right angles) with the projection plane.
There are two types of oblique projections: Cavalier and Cabinet. The Cavelier projection makes 45 angle with projection plane whereas In Cabinet projection, the projection of a line perpendicular to the view plane has the same length as the line itself.
Usually when drawing, all the three axes of the oblique drawing are constructed in which one axis is horizontal and the other is vertical while the third axis is from 30 to 60 to the horizontal line. At least two views of orthographic projection are selected.
Oblique projection is commonly used in technical drawing.
Oblique drawings are also used in engineering and design. The object is drawn with the most distinguishing features facing towards the observer, showing true shape of these features.

## Slide 19
BASIS OF COMPARISON | ORTHOGRAPHIC PROJECTION | OBLIQUE PROJECTION
Description | Orthographic projection can also be described as a two-dimensional graphic representation of an object in which the projecting lines are at right angles to the plane of the projection. | Oblique projection can also be described as a parallel projection in which the projection lines are not orthogonal to the projection line.
Form | It is a form of parallel projection | Oblique projection is a form of parallel projection.
Types | Isometric Projection Diametric Projection Trimetric projection | Cavalier Projection Cabinet Projection
Projector Lines | The projector lines intersect the plane being projected on to at a perpendicular angle (thus, they are orthogonal). | The projector lines form oblique angles (non-right angles) with the projection plane.
Application | Used by engineers, designers, architects and technical artists. | Commonly used in technical drawing.

## Slide 21
PERSPECTIVE PROJECTION
In Perspective Projection the center of projection is at finite distance from projection plane. This projection produces realistic views but does not preserve relative proportions of an object dimensions. Projections of distant object are smaller than projections of objects of same size that are closer to projection plane. The perspective projection can be easily described by following figure :
Center of Projection –
It is a point where lines or projection that are not parallel to projection plane appear to meet.
View Plane or Projection Plane –
The view plane is determined by :
View reference point R0(x0, y0, z0)
View plane normal.
Location of an Object –
It is specified by a point P that is located in world coordinates at (x, y, z) location. The objective of perspective projection is to determine the image point P’ whose coordinates are (x’, y’, z’)

## Slide 22
Types of Perspective Projection :
Classification of perspective projection is on basis of vanishing points (It is a point in image where a parallel line through center of projection intersects view plane.). We can say that a vanishing point is a point where projection line intersects view plane.
The classification is as follows :

## Slide 23
One Point Perspective Projection – One point perspective projection occurs when any of principal axes intersects with projection plane or we can say when projection plane is perpendicular to principal axis.
In the above figure, z axis intersects projection plane whereas x and y axis remain parallel to projection plane.

## Slide 24
Two Point Perspective Projection – Two point perspective projection occurs when projection plane intersects two of principal axis.
In the above figure, projection plane intersects x and y axis wheres z axis remains parallel to projection plane.

## Slide 25
Three Point Perspective Projection – Three point perspective projection occurs when all three axis intersects with projection plane. There is no any principle axis which is parallel to projection plane.

## Slide 26
Application of Perspective Projection : The perspective projection technique is used by artists in preparing drawings of three-dimensional objects and scenes.